Thermal cut – out  AE09

### Contact							 normally closed

### Rated voltage   				 	max 250 V, 50(60 Hz

### Rated current

### of resistance loading Izn, cos( = 1,0	2,5A

### of resistance and induction loading Ix, cos( = 0,6           	1,6 A

### Number of operating cycles at rating loading               10 000 cycles

Maximum loading/number of automatic cycles              3,6 A / 2 000 cycles

### Range	 of rated switching temperatures             	650C - 1600C

### Operating temperature tolerance			             ±5K  / ±7,5K  /  ±10K

### Operating differential                               		 30 ( 150C

### below switching temperature

### Speed of temperature changes

### to determine switching temperature			0,50C / min

Maximum ambient temperature   				1800C

Degree of protection                                         		IP 00

### PTI of material used for insulation			 250V

### Insulation resistance 					( 2 M(

### Electrical strength of insulation				2 500 V; 50 Hz; 1 min.

Contact resistance                              			( 40 m(

Construction							for incorporation

TOMIC S.A

ul. Żeromskiego 76/82

09 – 300 Żuromin

Poland

# Text boxes

Tel. +48 23 657 31 61, +48 23 657 31 19

Fax: +48 23 657 24 07

e –mail: tomic@home.pl

http:// www. tomic.home.pl

## Electrical scheme